# JR-CNC-Q3015钻铣磨加工中心配置表

# Specification of JR-CNC-Q3015 drilling, milling and grinding machining center

| 机型Model | 3015 |
| --- | --- |
| 行程 (轴心) Stroke (axis) | X轴 X axis | 3150MM |
|  | Y轴Y axis | 1600MM |
|  | Z轴Z axis | 120MM |
|  | 主轴鼻端至工作台 Spindle nose to table | 55 |
| 工作台 (25MM6061铝） Working table | 铝板工作台尺寸 working table size | 3000*1500 |
|  | 最大荷重Maximum load | 650KG |
|  | 自铣工作台 Self-milling table | 平面吸附 Plane adsorption |
| 机体方钢 Body square steel | 焊接,热处理,震动时效Welding, heat treatment, vibration aging | 300*200*15 200*200*8 |
|  | 不锈钢板材 Stainless steel sheet | 1 .5MM-2MM |
| 主轴 Spindle | 磨轮孔直径 Wheel hole diameter | 22mm |
|  | 转速Rotating speed | 2000- 12000 |
|  | 驱动方式Drive way | 伺服驱动 Servo drive |
|  | 培林润滑系统 Bearing Lubrication System | 高温黄油High temperature butter |
|  | 冷却系统cooling system | 水冷Water cooling |
|  | 主轴马力 Spindle power | 15KW+变频器 15KW+ inverter |
|  | 四轴伺服马力 Four-axis servo horsepower | 4*1.5KW |
| 进给速度 Feed rate | X.Y轴快速 X. Y axis speed | 11M/m in |
|  | Z轴快速 Z axis speed | 6M/m in |
|  | 最大切削速度 Maximum cutting speed | 11M/m in |
| 精度 Precision | 定位精度 positioning accuracy | + 0.05 |
|  | 重复精度 Repeatability | 0.02 |
|  | 产品精度 Product accuracy | 0.02mm |
| 加工范围 Processing range | Max GlassSize(mm)3000* 1500 | Min Glass Size(mm)50*50 |
|  | 加工厚度 Glass Thickness | 2mm-20mm |
| 重量Weight | 重量Weight | 4000KG |
|  | 耗电量 power | 15KW |
|  | 占地面积(长*宽*高) Machine Size | 4.5*2.9*1.8M |
| 主要配件 Main Components | 主轴Spindle | 华雕Huadiao |
|  | 伺服电机/驱动器servo motor | VEICHI 总线绝对值 （德国编码器） VEICHI bus absolute value (German encoder) |
|  | 直线导轨/丝杆 Linear guide/screw | 台湾TB I Taiwan TBI |
|  | 系统system | 深圳奇芯 Shenzhen Qixin |
|  | 润滑泵Lubrication pump | 全 自动润滑 Automatic lubrication |
|  | 真空泵Vacuum pump | 上海 Shanghai |
| 附件 | 吸盘16个 定位6个 16 suction cups Locate 6 | 硅胶密封圈+尼龙柱 （ 自吸式）Silicone sealing ring + nylon column (self-priming) |
| 刀库 | 直排刀库 In-line tool magazine | 7个刀位 7 tool positions |
|  | 使用说明书，user's manual | 伺服说明书全套 Servo manual |

设备简介：Equipment introduction:

产品功能：适用于玻璃、岩板、石材等硅酸盐材质的产品的磨边及抛光和钻铣磨。

Product function: suitable for edging and polishing and drilling 、milling of silicate materials such as glass, slate and stone.

设备占地面积：15平方米Equipment area: 15 square meters

操作人员： 开机：1人（懂电脑基本操作）

大版上片：2人（有搬运经验）

Operator:  1 person (understand the basic operation of computer)

Large-scale loading: 2 people (with handling experience

产品特点：

- 总线绝对值伺服电机、进口高精度齿条等顶级元气件配置有效地保障磨边精度及稳定性，使用寿命更长，能满足各种形状的磨边和抛光；Bus absolute value servo motor, imported high-precision rack and other top-level components can effectively ensure the accuracy and stability of edging, and have a longer service life, which can meet the edging and polishing of various shapes;

- 双工位磨边功能，大幅提机器的工作效率；Double-station edging function, greatly improve the working efficiency of the machine;

- 高智能定位，极大程度地提高产品更换厚度和形状的定位时间；Highly intelligent positioning, greatly improving the positioning time of product replacement thickness and shape;

- 磨边机的自动注油和功能，有效保证机器运行的润滑，防止传动部分磨损过快；The automatic oil filling and function of the edger can effectively ensure the lubrication of the machine operation and prevent the transmission part from wearing too fast;

- 对操作人员无特殊要求，操作简单，便于管理。No special requirements for operators, simple operation and easy management.

- 采用BT40刀柄，一键更换磨轮的速度为30秒内。Using BT40 handle, the speed of one-key replacement of grinding wheel is within 30 seconds.

设备配置：Device Configuration:

（1）、整机材料选用国家标准含锰型材桥梁钢（Q345A）焊接成型并经过时效处理，此类钢材综合力学性 能良好，塑性和焊接性能良好。表面经过特殊除锈工艺去除表面锈斑和表氧化层，底层喷高级锌黄底聚酯漆，表面喷涂高级汽车漆。The material of the whole machine is made of national standard manganese-containing profile bridge steel (Q345A), welded and formed and subjected to aging treatment. This type of steel has good comprehensive mechanical properties, good plasticity and welding properties. The surface undergoes a special rust removal process to remove the surface rust spots and surface oxide layer, the bottom layer is sprayed with high-grade zinc yellow primer polyester paint, and the surface is sprayed with high-grade automotive paint.

（2）、真空系统设计合理，真空度高，吸取工件快，可靠性高，真空压力SMC品牌。The design of the vacuum system is reasonable, the vacuum degree is high, the workpiece is absorbed quickly, the reliability is high, and the vacuum pressure is SMC brand.

（3）、设备具有一键复位功能，只需按一下触摸屏就能完成自动启动之前的所有准备工作，大大提高工作效率。设备具有故障报警及安全报警装置。The device has a one-key reset function, and all preparations before automatic startup can be completed by simply pressing the touch screen, which greatly improves work efficiency. The equipment has fault alarm and safety alarm devices.

软件：software:

Windows操作界面，并在控制台上操作；Windows operation interface, and operate on the console;

自安装使用起，即可全记录所有设备程序、生产任务、图形等From installation and use, all equipment programs, production tasks, graphics, etc. can be fully recorded

可统计当日工时，磨边数量，以便于每班工作数量的记录It can count the working hours of the day and the number of edging, so as to facilitate the record of the number of work per shift

可与AUTO CAD 绘图软件配套兼容Compatible with AUTO CAD drawing software

自带上百图案，可随意编辑使用Comes with hundreds of patterns, which can be edited and used at will

运行速度快，运行平稳，控制精度高，控制器结构模块化Fast running speed, stable running, high control precision, modular controller structure

完整的玻璃压力库存储，一次性将各规格厚度的切割压力输入保存后，可以直接调用；The complete glass pressure library is stored, and the cutting pressure of each specification and thickness can be input and saved at one time, and can be called directly;

加工路径实时跟踪显示，适时记录运动坐标，轴状态，I/0状态，故障诊断与报警自动记录Real-time tracking display of processing path, timely recording of motion coordinates, axis status, I/0 status, automatic recording of fault diagnosis and alarm

完整的刀具补偿功能，不同的磨轮有自己的磨削速度，自动调整压力值Complete tool compensation function, different grinding wheels have their own grinding speed, automatically adjust the pressure value

人机界面简洁大方，参数调整简单，需要操作人员修改的参数较少，简单直观，对操作员要求低The man-machine interface is simple and elegant, the parameter adjustment is simple, and the parameters that need to be modified by the operator are few, simple and intuitive, and the requirements for the operator are low

各种保护：包括软硬限位、刀压限制、外部急停控制等等Various protections: including soft and hard limit, tool pressure limit, external emergency stop control, etc.

关键部分图片key part images

| 电路柜cabinet |  |
| --- | --- |
| 水箱潜水泵 water tank submersible pump |  |
| 丝杆screw |  |
| 油泵及过滤器 Oil pump and filter |  |
| 主轴防水裙 Spindle waterproof skirt |  |
| 吸盘 sucker |  |
| 分油器及气路管 Oil separator and gas pipeline |  |
| 电机及丝杆座 Motor and screw seat |  |
| 主轴变频器 Spindle frequency converter |  |
| 气路柜 Gas cabinet |  |
| 真空泵 vacuum pump |  |
| 冷水机 chiller |  |
| 驱动器 Driver |  |
| 主轴 Spindle |  |
| 压力罐 pressure tank |  |
| BT40刀柄 BT40 handle |  |
| 直排刀库 In-line tool magazine |  |

# Text boxes

-

-