PROMOLD

805

Antimould & Humid Paint

PRODUCT DESCRIPTION:

It is a water and acrylic emulsion based, very strong insulation paint that is modified with special chemicals and polymers, produced for resolving of problems of moisture and mold occured on interior and exterior walls of buildings.

FEATURES:

PROMOLD prevents mold formation in dry film on the surface.

It has high covering power.

Adherence is high.It is Matt.

Easy to apply. Environment friendly.

PRODUCT INFORMATION:

Chemical Structure 		Acrylic based / Water based

View / Color 			Liquid / Contact

pH 				7-10

Density 			1.30 ± 0.2 g / cm3

# PERFORMANCE:

(23°C, %50 Relative Humidity)

Brightness		G3	TS 4318 EN ISO 2813

Grain Size		S1	TS 2620 EN ISO 1524

These values are obtained as a result of laboratory tests and are valid for the performance of finished applications at the end of full drying time. Since the temperature and humidity values in the construction site and the application surface vary, given values might be diversing.

APPLICATION AREAS:

In the interior and exterior walls, in the subbasements of the buildings,

In basements, garages or cellars

Inside walls facing north

It is used in areas with many moisture and humid.

PROMOLD

805

Antimould & Humid Paint

APPLICATION INSTRUCTIONS

The surface should be cured, dry and sound. Remove oil, grease, dirt, paint and salt vapors that would prevent adhesion. All cracks, joints, skirts and damaged infiltration areas must be repaired.

Add about 20% water and mix with a low speed mixer.

Repair of damage during use is very easy and economical. It is applied in two coats. After the first coat, wait for 24 hours to dry and then discard the second layer.

# LIMITATIONS:

To achieve optimum quality, please follow the instructions for use. It should not be applied in very windy, rainy weather which is directly exposed to sunlight at very high temperature. Do not apply on surfaces with frost hazard. Application should be between +5 C and +30 C. Do not apply at temperatures below 5 ° C. The product must be protected from rain, water, frost and adverse external influences until curing (28 days).

# CONSUMPTION:

300-400 gr / m2

# PACKING:

1 kg plastic drum

3 kg plastic drum

5 kg plastic drum

18 kg plastic drum

# SHELF LIFE:

It is 1 year from the production date in the original package in dry and humid-free (+5 C to +25 C temperature) environments. The lid of the containers should be tightly closed when not in use. Keep away from moisture.

STORAGE CONDITIONS:

It should be stored in its original unopened package in a cool, dry and humid-free (+5 C to +25 C temperature) environment. Should not be left in direct sunlight.

# SAFETY:

Avoid contact with skin and eyes. Wear protective gloves, glasses, mask and clothing. In case of eye contact, consult a doctor immediately. Keep out of the reach of children. Avoid skin contact. Do not swallow. Keep away from sources of ignition. For further information and advice, please refer to the Safety Data Sheet.

DEKOSTAR San. Ve Tic. Ltd. Sti. İs not responsible of application mistakes resulted from misuse or usage without following the instructions and suggestions of DEKOSTAR reserves the right to change its products. Users should consider the lastest edition of the Techical Data Sheet of the product.